## Slide 1: ParisSimulator Project

## Slide 2
Project participants
- Prof. Gretar Tryggvason , University of Notre Dame
- Dr Sadegh Dabiri, , University of Notre Dame
- Stéphane Zaleski, ∂’Alembert
- Ruben Scardovelli, Univ of Bologna, Italy
- Phil Yecko, Montclair, NJ, USA

## Slide 3
ParisSimulator: Paralllel Robust Interface Simulator
Aims:
1) To have a relatively simple code on which to test ideas about VOF,
parallelisation, Front Tracking, Lagrangian Particles. Use relatively simple
algorithms and programming techniques.
2) To perform certain types of large scale computations relatively fast
thanks to a simple mesh structure.
3) To serve as a backup to Gerris in case unsolvable bugs are encountered in certain applications.
Released as a free code under GPL.
80% based on FTC3D2011, a code by Gretar Tryggvason and Sadegh Dabiri,
20% on Surfer, by Stephane Zaleski, Ruben Scardovelli, Jie Li and Gianluigi Zanetti.

## Slide 4
Numerical Methodology
- Finite Volume/ Finite Difference on a Cartesian Grid with streched x, y, z coordinates.
(stretched coordinates will not be available immediately for VOF)
- MAC grid.
- Time schemes : 1) first order Euler 2) second order Runge-Kutta for NS part
- Advection terms by QUICK (next slide)
- explicit or implicit viscous terms.
- VOF - PLIC – CIAM for interface reconstruction and advection (in the first version we just use the relatively simple VOF methods in Surfer)
- Surface tension by elementary Continuous Surface Stress method as in Surfer (in the
first version).

## Slide 5
Numerical Methodology (continued)
- solids by blocking solid sites. Solid sites can be blocked at each step of time-marching
and pressure correction (Poisson solve), so they are always and exactly zero.
- MPI with an adjustable number of ghost layers (two in the present implementation).
- Two boundary types: solid wall or periodic.
Input and output
- Input of parameters by FORTRAN namelist.
- No input format for for geometrical objects so far.
- Output format: vtk and visit or tecplot (tecplot should be added for VOF)

## Slide 6
Code style, writing and management
- Code entirely in Fortran90 except for some test scripts outside of the main code.
- All of FTC3D2011 (base version without front tracking) is contained in two f90 files ! Choice made to keep the number of files low.
- no configure, only a short Makefile. But C users beware, f90 compilation involves a different dependency structure.

## Slide 7
#--------- paris-ParisSimulator main Makefile --------------------------
FC = mpif90
# select option for hypre
# default hypre installation without root privileges:
# HYPRE_DIR = $(HOME)/hypre-2.8.0b/src
# Macport installation in /opt
HYPRE_DIR = /opt/hypre
# babbage
# HYPRE_DIR = /share/apps/hypre
#------------------------No changes needed beyond this line --------------------------------------
HYPRE_LIBS = -L$(HYPRE_DIR)/lib -lHYPRE
Makefile

## Slide 8
OBJ = paris.o solids.o modules.o vofmodules.o front.o
SRC = $(wildcard *.h *.c *.f90)
INC = $(wildcard *.h)
install: $(OBJ)
@echo compiler is FC = $(FC), mpi override is OMPI_FC = $(OMPI_FC)
$(FC) -o paris $(FOPTS) $(OBJ) $(HYPRE_LIBS)
mv paris ~/bin/paris
all: tags install
clean:
@rm -fR *.o *.mod paris stats *~ track out* errftc tmp* *.tmp fort.* *.visit core.* statsbub
@cd Tests; sh ./clean.sh; cd ..
@cd Documentation; make clean; cd ..
test: install compare
@echo "This test takes approximately 1 minute on a 4-core intel i7 MacBookPro"
@cd Tests; chmod +x ./runtests.sh; ./runtests.sh
Makefile - continued

## Slide 9
tags: $(SRC)
# @SZ Create a tags file named TAGS for use by emacs
@etags $(SRC)
# @SZ Create a tags file named tags for use by vi or textwrangler
# @SZ On MacOS tags and TAGS are identical !
# @SZ ctags paris.f90
paris.o: paris.f90 solids.o modules.o
$(FC) -c $<
solids.o: solids.f90 modules.o
$(FC) -c $<
%.o : %.f90
$(FC) -c $<
.c.o: $< $(INC)
$(CC) -c $(CFLAGS) $<
Makefile - end

## Slide 10
- paris-stable has now 5335 lines in four source files (April 9, 2013).
- darcs archive (available at http://www.ida.upmc.fr/~zaleski/darcs/paris-stable )
- no documentation

## Slide 11
HYPRE Poisson solver: PFMG solver ( a geometric solver usable on structured
grids, unlike Boomer AMG used in Gerris and on unstructured grids. )

## Slide 12
Scaling tests: weak scaling in CUPS per core, babbage cluster (AMD, d’Alembert)

## Slide 13
Scaling in CUPS,
all machines